UHF rfid integrated reader                                                         OPP-D07

387*277*23.3MM

- Toughened glass panel, beautiful and fashionable

- Exclusive antenna, accurate reading range

- USB drive free (windows, Android)

- It has the function of audible and visual alarm

- The device is available in black and white

1.The synopsis of the reader：

OPP-D07 is a high-performance RFID reader with fashionable appearance. It integrates high-performance RFID modules and adopts a uniquely designed antenna, which can accurately control the reading range and realize the rapid reading and writing processing of electronic tags while maintaining a high reading rate. It can be widely used in RFID applications such as cashier, jewelry inventory, warehousing and logistics, books and archives, workstation, judicial voucher and so on.

2.Product parameters：

| Mechanical electrical performance |
| --- |
| Dimension：（MM） | 387（L）*277（W）*23.3（H）（±1） |
| Diemension including packaging（MM） | 445（L）*342（W）*63（H）（±3） |
| Net weight： (KG) | 1.73（±0.01） |
| Gross weight：（KG） | 2.02（±0.02） |
| Shell | Surface: tempered glass, bottom shell: ABS+PC |
| RF Antenan | ≥7dB, the uniquely designed antenna can accurately control the reading range |
| Performance Index |
| Transponder Protocols | EPCglobal Gen 2 (ISO 18000-6C) |
| Frequency | 865~868MHz/902～928MHz（Can be adjusted according to different countries or regions）） |
| Frequency modulation | FHSS or fixed-frequency, can be set by software |
| RF output | from 0 dBm to 26dBm* with +/-1dBm |
| Reading distance | ＞4m（eg.9662，depends on tag） |
| Peak inventory speed | >50 tags/sec |
| Tag RSSI | Supported |
| Power | USB drive free (windows, Android)5V,400mA,2W（MAX） |
| Communication interface | USB 2.0 |
| API Support | C#、JAVA |
| Environment |
| Operating Temp | -20～+55℃ |
| Storage Temp | -20～+85℃ |
| Humidity | 5%～95%RH，Non-condensing |